## Slide 1
Command and Control Data Link Subsystem(UL.32, STANAG-4703)(1/2)
-Minimum flight and navigation information
: indicated airspeed - 적용
: ground speed - 적용
: pressure altitude and related altimeter setting -미적용
: heading - 적용
: track - 미적용
: UA position on a map at a scale selectable by the operator
;A flight path deviation warning must be displayed and the appropriate procedure
must be established -미적용
: deviation between the planned ground track & the actual UA flight path -미적용
: UA position relative to the LOS data link transmitter/receiver displayed in terms of range,
bearing and altitude -미적용
: Where semi-automatic flight control modes are activated, the commanded flight/navigation
parameters sent to the UAV must be displayed -적용
: Airspeed minimum and maximum limitations and corresponding speed warnings -미적용
: UA altitude -적용
: Vertical speed -미적용
: navigation system status -미적용
: g-meter -미적용
-The minimum propulsion system data
: for electric engines
; remaining level of battery charge -적용
: a means to indicate engine health status
; engine RPM -미적용
; case temperature -미적용
; corresponding caution and warning alerts when specified minimum/maximum
limitations are being approached, reached, and/or exceeded -미적용
REF : NSA, “STANAG 4703 Edition 1: Light Unmanned Aircraft Systems Airworthiness Requirements (USAR-LIGHT), Final Draft“, NATO Standardization Agency, 2011

## Slide 2
Command and Control Data Link Subsystem(UL.26, STANAG-4703) (2/2)
-Uplink, Downlink
-Downlink must include
: Navigational information -적용
: Response to UA crew commands -일부 적용
: Equipment operating parameters(UL.32) -일부 적용
-Warning cues should be provided to alert the operator of detrimental degradation in data link
capabilities such as
  : approaching antenna masking attitudes -미적용
  : approaching external interfering antennas -미적용
  : approaching maximum data link range -미적용
-In case of data link loss, an automatic reacquisition process must try to re-establish the command
and control data link in a time period
: a warning must alert the operator, and the applicant must specify whether the alert
will be audible, visual, or both
: the alert should sound/be displayed continoususly until acknowledged and extinguished
: loss strategy must be established
- 24개 주요 항목 중 17항목이 미적용되어 있음
REF : NSA, “STANAG 4703 Edition 1: Light Unmanned Aircraft Systems Airworthiness Requirements (USAR-LIGHT), Final Draft“, NATO Standardization Agency, 2011